## Slide 1: Assumption Parish Operational Situation Summary
Emergency Management:
  Parish Emergency Declared – 19 June 2012
    Extended 30 days on 05 December 2014
    Extended 30 days on 05 January 2015
    Extended 30 days on 05 February 2015
    Extended 30 days on 05 March 2015
  State Emergency Declared – 3 August 2012
  LA Hwy 70 Open for traffic
  Mandatory Evacuation still in effect
  Security plans in place to secure sinkhole area
  Parish continues blog to inform residents
  Texas Brine issuing financial assistance for residents
  Bayou Corne Incident Command Center - HOTLINE 1-877-281-7311
  Facilitating the askGOHSEP@la.gov for questions
  APOEP and Sheriff’s Office relocated Command Post to 1424 Hwy 70S

## Slide 2: Assumption Parish Operational Situation Summary
Public Safety:
  LSP providing air craft support
  LSP providing HAZMAT support to parish as needed
  LDWF providing air boat support to parish as needed
  No market or recreational hunting or fishing in restricted area
  LSA Command Post on site
  An office trailer has replaced the GOHSEP vehicle and will serve as a consolidated command post for the Assumption Unified Command
  All state agencies currently involved with the event will continue to be in attendance.
  GOHSEP has added a notification widget to their website indicating the current alert level for OG-1 and Hwy 70

## Slide 3
Assumption Parish Operational Situation Summary
Gas Volumes as of 25 Mar
Vent Well Flare Data (24-hr pd Ending 1 pm on 3/24/2015) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Well | Reading Date | Reading Time | Well Operational Status | Flow Total End Date | Start Time | End Time | Time/Hours | Choke Size (1/64") | Dishcharge Orifice (Inch) | Static (PSIG) | Diff. (PSIG) | Diff. (Inch) | Gas Rate (MCF/H) | Gas Rate (MCF/D) | Cumulative Gas Flared (MCF) | Previous Flared (MCF Total) | SIWHP (PSI) | FWHP (PSI) | Comments
ORW-01 | 3/24/2015 | 7:51 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 1,099 | 1,099 | 0.0 |  | .
ORW-02 | 3/24/2015 | 7:53 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 1,680 | 1,680 | 0.0 |  | .
ORW-03 | NA |  | plugged | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | Plugged 1/27/2015
ORW-04 | 3/24/2015 | 7:34 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 1,082 | 1,082 | 35.0 |  | .
ORW-05 | NA | NA | plugged | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | Plugged 1/27/2014.
ORW-06 | 3/24/2015 | 7:41 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 1,097 | 1,097 | 7.5 |  | .
ORW-07 | NA | NA | plugged | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | Plugged 2/7/2014.
ORW-08 | NA | NA | plugged | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | Plugged 2/5/2014.
ORW-09 | 3/24/2015 | 7:40 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 1,037 | 1,037 | 13.0 |  | .
ORW-10 | 3/24/2015 | 7:45 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 568 | 568 | 0.0 |  | .
ORW-11 | 3/24/2015 | 7:33 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 112 | 112 | 1.0 |  | .
ORW-12 | NA | NA | plugged | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | Plugged 7/15/2013.
ORW-13 | 3/24/2015 | 7:22 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 1 | 1 | 0.0 |  | .
ORW-14 | 3/24/2015 | 7:18 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 1,588 | 1,588 | 9.0 |  | .
ORW-15 | 3/24/2015 | 7:54 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 1,531 | 1,531 | 0.0 |  | .
ORW-16 | 3/24/2015 | 7:48 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.250 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 199 | 199 | 2.0 |  | .
ORW-17 | 3/24/2015 | 7:43 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 62 | 62 | 0.0 |  | .
ORW-18 | 3/24/2015 | 12:10 PM | open | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0.5 | 0.063 | 0.10 | 0.00 | 1.00 | 0.00 | 0.10 | 91 | 91 |  | 3.0 | .

## Slide 4
Assumption Parish Operational Situation Summary
Gas Volumes as of 25 Mar
ORW-19 | 3/24/2015 | 7:44 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 213 | 213 | 20.0 |  | .
ORW-21 | NA |  | Plugged | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | Plugged 7/17/15
ORW-22 | 3/24/2015 | 8:01 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 1,063 | 1,063 | 0.0 |  | .
ORW-23 | 3/24/2015 | 8:00 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 110 | 110 | 0.0 |  | .
ORW-24 | 3/24/2015 | 7:59 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 298 | 298 | 18.5 |  | .
ORW-27 | NA |  | plugged | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA |  |  | Well tree valve closed 100% and locked 11-20-2013
ORW-26 | 3/24/2015 | 7:36 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 173 | 173 | 1.0 |  | Phase 4 Vent test.
ORW-28 | 3/24/2015 | 7:58 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.625 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 28 | 28 | 5.0 |  | .
ORW-29 | 3/24/2015 | 7:56 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 59 | 59 | 15.0 |  | Phase 4 vent test.
ORW-30 | 3/24/2015 | 7:37 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.625 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 42 | 42 | 3.0 |  | .
ORW-31 | 3/24/2015 | 7:35 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 13 | 13 | 7.0 |  | .
ORW-32 | 3/24/2015 | 7:52 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 90 | 90 | 0.0 |  | .
ORW-33 | NA |  | plugged | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | Plugged 1/20/2015
ORW-36 | 3/24/2015 | 12:23 PM | open | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 6.25 | 0.250 | 0.10 | 0.00 | 2.00 | 0.09 | 2.18 | 5,572 | 5,570 |  | 14.0 | .
ORW-37 | 3/24/2015 | 8:10 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 247 | 247 | 2.0 |  | .
ORW-38 | NA | NA | plugged | NA | 1:00pm | 12:00Pm | 24 | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | Plugged 2/16/2015.
ORW-39 | 3/24/2015 | 7:31 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 105 | 105 | 45.0 |  | .
ORW-40 | 3/24/2015 | 7:32 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.125 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 117 | 117 | 1.0 |  | .
ORW-41 | 3/24/2015 | 7:30 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0 | 0 | 0.0 |  | .

## Slide 5
Assumption Parish Operational Situation Summary
Gas Volumes as of 25 Mar
ORW-42 | 3/24/2015 | 12:00 AM | NA | 3/24/2015 | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA | NA |  | 0.0 | Disconnected 12/5/2013. Now PMW 19S.
ORW-43 | 3/24/2015 | 7:25 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 13 | 13 | 0.0 |  | .
ORW-46 | 3/24/2015 | 12:26 PM | open | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0.5 | 0.063 | 0.10 | 0.00 | 3.33 | 0.01 | 0.18 | 805 | 805 |  | 27.0 | .
ORW-48 | 3/24/2015 | 12:04 PM | open | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 2.75 | 0.063 | 0.10 | 0.00 | 6.68 | 0.01 | 0.25 | 1,888 | 1,888 |  | 9.5 | Long term pumping. Pump Check. Rocked choke.
ORW-49 | 3/24/2015 | 8:16 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0.00 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 546 | 546 | 9.0 |  | .
ORW-50 | 3/24/2015 | 12:20 PM | open | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0.5 | 0.063 | 0.10 | 0.00 | 1.00 | 0.00 | 0.10 | 1,550 | 1,550 |  | 11.0 | .
ORW-51 | 3/24/2015 | 12:17 PM | open | 3/24/2015 | 1:00pm | 12:00Pm | 25 | 1.25 | 0.063 | 0.10 | 0.00 | 4.31 | 0.01 | 0.20 | 50.0 | 49.76 |  | 7.0 | .
ORW-52 | 3/24/2015 | 8:21 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 289 | 289 | 0.0 |  | .
ORW-53 | 3/24/2015 | 8:23 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 89 | 89 | 31.5 |  | .
ORW-54 | 3/24/2015 | 12:06 PM | open | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 8.25 | 0.250 | 0.10 | 0.00 | 1.15 | 0.07 | 1.63 | 2,334 | 2,332 |  | 4.0 | Long term pumping. Pump check. Rocked choke.
ORW-55 | 3/24/2015 | 12:28 PM | open | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 6.5 | 0.250 | 0.10 | 0.00 | 2.00 | 0.09 | 2.13 | 3,007 | 3,005 |  | 23.0 | Drained 225 gallons from KO.
ORW-56 | 3/24/2015 | 8:24 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 69 | 69 | 5.0 |  | .
ORW-57 | 3/24/2015 | 12:00 PM | open | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 9.5 | 0.250 | 0.10 | 0.00 | 4.01 | 0.13 | 3.08 | 2,975 | 2,972 |  | 10.0 | Long term pumping. Pump Check.
ORW-58 | 3/24/2015 | 8:09 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 17 | 17 | 0.0 |  | .
OGRW-01 | 3/24/2015 | 7:25 AM | shut in | 3/24/2015 | 1:00pm | 12:00Pm | 25 | 0 | 0.063 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 5,245 | 5,245 | 8.0 |  | .
GOW-9-1 | 3/24/2015 | 12:00 AM | open | 3/24/2015 | 1:00pm | 12:00Pm | 24 | 7.75 | 0.250 | 0.03 | 0.00 | 7.04 | 0.09 | 2.20 | 47.74 | 45.54 |  | 7.3 | Choke reduced to 7.75

## Slide 6
Assumption Parish Operational Situation Summary
Gas Volumes as of 25 Mar
Well | Time Data Collected | Tbg Pressure (psig) | Csg Pressure (psig) | Notes
BC 2 | 8:04 | 4.5 | 7 | .
OG 1 | 7:27 | 362 | 369 | .
OG 2 | 7:24 | 97 | 100 | .
OG 3A | 7:19 | 448 | 471 | .
TBC 3 | 7:28 | 49 | 0 | .
PMW 004m | NM | NA | NM | .
PMW 004s | 8:14 | NA | 46 | .
PMW 007m | NM | NA | NM | .
PMW 007s | 8:17 | NA | 49 | .
PMW 008m | NM | NA | NM | .
PMW 008s | 7:48 | NA | 0 | .
PMW 012m | NM | NA | NM | .
PMW 015m | NM | NA | NM | .
PMW 015s | NM | NA | NM | code 3/not monitored
PMW 016m | NM | NA | NM | .
PMW 016s | 7:17 | NA | 54 | .
PMW 017m | NM | NA | NM | .
PMW 017s | 7:20 | NA | 55 | .
PMW 018m | NM | NA | NM | .
PMW 018s | 8:22 | NA | 2.5 | .
PMW 019s | 7:55 | NA | 4 | .
PMW 020m | NM | NA | NM | .
PMW 020s | 8:25 | NA | 46.5 | .
*Note: Cumulative gas flared for OGRW-1 represents combined gas flow from ORW-12 and TBC-RW-1 for all dates preceding March 4, 2013. Cumulative gas flared after March 4, 2013 represents only OGRW-1 (formerly TBC-RW-1).
*Note: Total daily gas flared and cumulative gas flared is based on data through 12pm of previous day
*Note: ORW-42 became a PMW on 10/2/13 ORW-42 is now PMW-019S
*Note: PMW-012S became a ORW on 9/6/13 PMW-012S is now ORW-54
*Note: PMW-018 Flared for 50 MCF on 11-22-13 through flare 6 during the emergency response to mitigate gas kicks developed during well construction
*Note: PMW-018 Flared for 1.53 MCF on 12-3-13 and 12-5-13 for 2.96 MCF for depressurization
*Note: All well pressures are read daily including weekends and holidays with data submitted to conservationorder <conservationorder@LA.GOV> daily.

## Slide 7: Assumption Parish Operational Situation Summary
The State Agency is responsible for oversight of the following activities. Texas Brine and its contractors are performing operational response activities.
Routine weekly outfall sampling
Performed industrial water wells sampling and in-situ monitoring (12/16)
Conducted daily well readings and flare maintenance
Continued monitoring and maintenance of continuous dewatering of ORWs 40, 48, 54, and 57.
Completed 0.0 psi verification at ORW-43 (12/15)
Completed 1 Hour Depletion Confirmation Test at ORW-31; however, flare 3 was inadvertently shut down during the test. (12/16) Test will be repeated in the future.
Completed Phase 4 vent test at ORW 22 (12/16)
Sampled MRAA 06 and 09 (12/15)
Completed depletion test at ORW 26
Installed transducer in OG3A to depth of 2660’ (12/19). Pressure reading this morning was 1636 psi.
Completed monthly monitoring of GP wells (12/22)
Conducted daily well readings and flare maintenance
Continued monitoring and maintenance of continuous dewatering of ORWs 40, 48, 54 and 57
Completed modified 1-hr depletion test at ORW-26 (12/17), ORW-30 (12/18), and ORW-31 (re-test) (12/22)
Completed Gamma Ray logging of MRAAs 1D, 4D, 6D, 8D, and 9D (12/18 and 12/19)
Finished monthly MRAA well sampling (MRAA 1 and 8)
Routine weekly outfall sampling
Downloaded transducer data and manually measured water levels in MRAA water wells (12/23)
Conducted daily well readings and flare maintenance
Continued monitoring and maintenance of continuous dewatering of ORWs 40, 48, 54, and 57.
Performed monthly transducer downloads of ORWs, PMWs, and MRAA wells (12/25-26)
Routine weekly outfall sampling – two events (12/30 and 01/06)
Conducted daily well readings and flare maintenance
Continued monitoring and maintenance of continuous dewatering of ORWs 40, 48, 54, and 57.
Completed Phase 4 one month venting on ORW 28 (12/31)
Began (non-Phase 4 schedule) intermittent gas venting of ORWs 24 and 39 (01/06)
Continue (non-Phase 4 schedule) intermittent gas venting of ORWs 24 and 39 (01/07)
Adjusted choke settings on ORWs 36, 49 and 50 (12/31)
Adjusted choke settings on ORWs 19 and 56 (01/01)
Adjusted settings on flares 3, 5 and 6 (01/01)
Adjusted choke on ORW 54 (01/06)

## Slide 8: Assumption Parish Operational Situation Summary
The State Agency is responsible for oversight of the following activities. Texas Brine and its contractors are performing operational response activities.
Collected weekly LPDES outfall samples (1/14)
Conducted daily well readings and flare maintenance
Continued monitoring and maintenance of continuous dewatering of ORWs 40, 48, 54, and 57. (ORW-40 pump turned off on 1/7 for freeze protection)
Completed zero verification test at ORW-1 and ORW-2; Confirmed 0 psi (1/12)
Shut in GOW-9-1; no gas flow (1/12)
Began quarterly MRAA Well sampling (1/12); work is ongoing
Completed Phase 4 vent test on ORW-15; initial WH pressure @ 0.8 psi (digital gauge); connected digital flow meter, open well at 6.0 choke setting; no gas flow recorded (1/13)
Collected monthly gas samples from flares (1/13)
Began quarterly vent test of PMWs (1/14); work is ongoing
Began quarterly bubble site monitoring (1/14); work is ongoing
Performed quarterly geoprobe monitoring (1/8)
Collected weekly LPDES outfall samples (1/20)
Conducted daily well readings and flare maintenance
Continued monitoring and maintenance of continuous dewatering of ORWs 40, 48, 54, and 57. (ORW-54 shut in on 1/19 to facilitate PMW-19S vent test)
Completed zero verification test at ORW-21 and ORW-38; Confirmed 0 psi (1/15)
Opened GOW-9-1 to flare after 1 week shut-in (1/20)
Completed quarterly MRAA Well sampling (1/21)
Completed Phase 4 vent test on ORW-30; initial WH pressure @ 1.3 psi (digital gauge); no gas flow recorded on digital flow meter (1/19)
Completed Phase 4 vent test on ORW-31; initial WH pressure @ 39.3 psi (digital gauge); recorded 53.5 SCF gas flow over 23 minute period; monitored an additional 104 minutes with no change; final WH pressure = 0.0 psi (1/20)
Completed Phase 4 vent test on ORW-26; initial WH pressure @ 2.4 psi (digital gauge); recorded 0.491 SCF gas flow over 3 minute period; monitored an additional 71 minutes with no change; final WH pressure = 0.0 psi (1/20)
Began the P&A of ORW-33 (1/19)
Began the P&A of ORW-3 (1/20)
Began the monthly monitoring of PVWs and KGC (1/20)
Redeveloped PVW-26-6 and PVW-26-10 (1/21)
Completed quarterly vent test of PMWs (1/21)
Completed quarterly bubble site monitoring (1/16)
Completed Industrial Well sampling (1/20)

## Slide 9: Assumption Parish Operational Situation Summary
The State Agency is responsible for oversight of the following activities. Texas Brine and its contractors are performing operational response activities.
Collected weekly LPDES outfall samples (1/27)
Conducted daily well readings and flare maintenance
Continued monitoring and maintenance of continuous dewatering of ORWs 40, 48, 54, and 57.
Redeveloped ORW-48 (1/21)
Completed the monthly monitoring of PVWs and KGCs (1/22)
Completed surface water sampling (1/22)
Completed Phase 4 vent test on ORW-29; well head pressure: 26.2; install digital gas flow meter, open choke to 6.0; recovered 41.228 SCF in 23 minutes; continue to monitor for an additional 79 minutes with no further gas flow recorded (1/23)
Completed Phase 4 vent test of ORW-32: well head pressure: 2.5; install digital gas flow meter, open choke to 6.0; recovered 0.347 SCF in 3 minutes; continue to monitor for an additional 106 minutes with no further gas flow recorded (1/26)
Completed P&A of shallow Geoprobe wells GP-ORW-06 (1/22), GP-ORW-09 (1/23), GP-ORW-16 (1/26), GP-ORW-17 (1/26), NSDMW013 (1/27), NSDMW014 (1/27)
Completed the P&A of ORW-33, ORW-3, DPVE-47-1, DPVE-47-2 and DPVE-47-3
Collected weekly LPDES outfall samples (2/03)
Began the quarterly sinkhole depth survey (1/30)
Completed monthly bubble site monitoring (2/03)
Collected gas samples from PVWs and KGCs (2/02)
Conducted daily well readings and flare maintenance
Continued daily monitoring and maintenance of continuous dewatering of ORWs 40, 48, 54, and 57.
Shut in GOW-9-1 (1/29)
Completed transducer downloads on ORWs
Redeveloped ORW-46 (1/28 & 29), ORWs-49 and 56 (2/02), ORW-50 (2/03)
Began redevelopment of ORW-06 (2/03)
Completed Phase 4 - zero pressure verification tests on ORW-21 and 38 (2/02) and 41 (2/03)
Completed Phase 4 – 30 day vent test on ORW-14 (2/02)
Completed Phase 4 - 3 month vent test on ORW-24 (2/03)
Completed P&A of shallow Geoprobe wells NSDWMs-07 and 09 (1/28), NSDWMs-04 and 016 (1/29), NSDWM-03 (1/30)
Collected weekly LPDES outfall samples (2/10)
Completed the quarterly sinkhole depth survey (2/10)
Completed the quarterly berms survey (2/09)
Completed the quarterly sinkhole profile water sampling (2/09)
Completed the weekly Outfall sampling (2/10)
Completed the monthly industrial water well sampling (2/10)

## Slide 10: Assumption Parish Operational Situation Summary
The State Agency is responsible for oversight of the following activities. Texas Brine and its contractors are performing operational response activities.
Conducted daily well readings and flare maintenance
Continued daily monitoring and maintenance of continuous dewatering of ORWs 40, 48, 54, and 57.
Completed transducer downloads on ORWs
Redeveloped ORW-06 (2/3, 4 and 5), ORW-10 (2/09)
P&A of Geoprobe wells NSDWM-08 (2/09), GP-22-02 and GP-22-03 (02/10)
Phase 4 – 3 month vent test on ORW22 (2/09) and 23 (02/10)
Completed the Phase 4 – 30 day vent test on ORW-16 (2/09)
Conducted daily well readings and flare maintenance
Continued daily monitoring and maintenance of continuous dewatering of ORWs 40, 48, 54, and 57.
Completed transducer downloads on ORWs
P&A of Geoprobe wells GP-37-01 and GP-37-02 (02/11), NSDMW-017 (2/12), NSDMW-006 (2/12)
Conducted 1-hr depletion test at ORW-10; no gas produced; 0.0 psi well head pressure; (2/13)
Completed Phase 4 vent test (3 month) on ORW-28; 0.447 SCF; (2/11)
Completed Phase 4 Zero Verification test of ORW-43; confirmed zero psi; (2/13)
Began P&A of ORW-21 and ORW-38 (2/16)
Completed quarterly sinkhole and berm survey
Collected weekly LPDES outfall samples; (2/18 and 2/24)
Collected gas samples from BS-1, BS-15 and BS-113 (2/18)
Began the monthly groundwater MRAA well sampling (2/24)
Conducted daily well readings and flare maintenance
Continued daily monitoring and maintenance of continuous dewatering of ORWs 40, 48, 54, and 57.
Completed weekly transducer downloads on ORWs
Completed the P&A for ORWs 21 and 38 (2/19)
Completed monthly flare gas sampling (2/18)
Completed monthly monitoring of KGC and PVWs (2/19)
Completed quarterly maintenance of RESPEC TM and WL instruments (2/19)
Completed workover (2/18) and depletion test (2/19) at OGRW-1
Performed Phase 4 zero verification test at ORW-11; Confirmed 2.2 psig of wellhead annulus pressure. (2/20)
Began monthly sampling of selected MRAA wells (2/23)
Conducted depletion test at ORW-9 (2/24)

## Slide 11: Assumption Parish Operational Situation Summary
The State Agency is responsible for oversight of the following activities. Texas Brine and its contractors are performing operational response activities.
Collected weekly outfall samples; (2/24 and 3/3)
Completed the monthly groundwater MRAA well sampling (2/27)
Completed monthly GP wells pressure monitoring (except GP-BS-15, GP-BS-23 and GP-BS-44) (2/27)
Completed monthly ORW transducer data download (3/2)
Conducted daily well readings and flare maintenance
Continued daily monitoring and maintenance of continuous dewatering of ORWs 40, 48, 54, and 57.
Completed weekly transducer downloads on ORWs
Continued enhanced gas production on ORW-55 (removed 1,540 gallons from 2/25 to 3/3)
Completed Phase 4 – 6 month zero pressure verification on: ORWs-01 and 02 (2/25); ORW-15 (2/26)
Completed Phase 4 – 30 day zero pressure verification on ORW-13 (2/27)
Performed Phase 4 – 1 month venting at ORW-11 (3/2)
Performed Phase 4 – 3 month zero pressure verification on ORW-17 (3/3)
Performed depletion confirmation test on ORW-4 (2/25) and began Phase 3A/3B dewatering (3/2)
Retrofitted GOW-9-1 with 4” well head (2/26) and installed 2” pump (3/2)
Collected weekly outfall samples; (3/3 and 3/10)
Completed the monthly groundwater MRAA well sampling (3/6)
Completed monthly GP wells pressure monitoring for GP-BS-15, GP-BS-23 and GP-BS-44) (3/4)
Completed monthly bubble site monitoring run (3/4)
Completed transducer data download and manual water level measurements on MRAA wells (3/10)
Conducted daily well readings and flare maintenance
Continued daily monitoring and maintenance of continuous dewatering of ORWs 40, 48, 54, and 57
Completed monthly leak testing for ORWs (3/4)
Completed weekly transducer downloads on ORWs
Continued enhanced gas production on ORW-55
Shut in ORW-57 at 12:18 PM and restarted pump/connected to flare at 4:34 PM (3/6)
Conducted extended depletion verification testing for ORW-4 (3/4 to 3/9)
Completed Phase 4 – 3 month venting on ORW-16 (3/9)
Continued GOW-9-1 dewatering (3/4 to 3/9); Removed pump for repair (3/9 and 10)
Installed pump in ORW-10 for additional depletion verification test setup (3/10)

## Slide 12: Assumption Parish Operational Situation Summary
The State Agency is responsible for oversight of the following activities. Texas Brine and its contractors are performing operational response activities.
Collected weekly outfall samples (3/17)
Completed monthly pressure monitoring of shallow GP wells (3/17)
Conducted daily well readings and flare maintenance
Continued daily monitoring and maintenance of continuous dewatering of ORWs 48, 54, and 57
Completed weekly transducer downloads on ORWs
Continued enhanced gas production at ORW-55
Completed ORW-10 depletion test; Removed 355 gallons in 6.6 hrs.; no gas produced (3/11)
Completed monthly Flare Gas sampling (3/16)
Completed Phase 4 – 3 month venting of ORW-30; no gas produced (3/17)
Continued GOW-9-1 dewatering; Removed pump and repaired (3/17)
Collected weekly outfall samples (3/14)
Conducted daily well readings and flare maintenance
Continued daily monitoring and maintenance of continuous dewatering of ORWs 48, 54, and 57
Completed weekly transducer downloads on ORWs
Continued enhanced gas production at ORW-55
Completed Phase 4 vent test of ORW-31 (3 Month); 48.8psi well head, open to 6.0 choke initially, then incrementally opened to 11.0; recorded 76.873 SCF of gas during the event (3/18)
Completed Phase 4 vent test of ORW-26 (3 month); 1.2psi, open to 6.0 choke, no gas recovered (3/23)
Completed Phase 4 vent test of ORW-29 (3 month); 13.0psi, open to 6.0 choke, the incrementally to 10.0; recorded 9.934 SCF of gas during the event (3/24)
Continued GOW-9-1 dewatering
Completed monthly monitoring of PVWs/KGCs
Completed monthly sampling of MRAA wells 1s, 1m, 1d, 9d, 5s, 5m, 5d (ongoing)

## Slide 13: Assumption Parish Operational Situation Summary
DHH / Office of Public Health
  Section for Environmental Epidemiology and Toxicology
    Air Monitoring Sample Data
      SEET has received and is analyzing community ambient air sampled 5/2/14, 5/6-7/14, 5/9/14, 5/13-14/14, 5/16/14, 5/20-21/14, 5/23/14, 5/27/14, 5/30/14, 6/3-4/14, 6/6/14, 6/13/14, and 6/17/14 (MultiRAE) and 5/22-27/14 (MAML). SEET will issue a letter to the parish in reference to these findings once the review of the data has been completed.
      SEET has received and is analyzing sample results for air at bubble sites collected 5/7/14, 5/14/14, 5/21/14, 6/4/14, and 6/17/14 (MultiRAE). SEET will issue a letter to the parish in reference to these findings once the review of the data has been completed.

## Slide 14: Assumption Parish Operational Situation Summary
DHH / Office of Public Health
  Section for Environmental Epidemiology and Toxicology
    Industrial Water Well Sampling Data
      No new water well data received during this operational period.

## Slide 15: Assumption Parish Operational Situation Summary
DHH / Office of Public Health
  Section for Environmental Epidemiology and Toxicology
    Slurry Water Sampling Data
      No new slurry data received during this operational period.

## Slide 16: Assumption Parish Operational Situation Summary
DHH / Office of Public Health
  Section for Environmental Epidemiology and Toxicology
    Surface Water at Bubble Sites
      No new surface water data received during this operational period.

## Slide 17
Department of Environmental Quality
Air monitoring for VOC’s continues with no dangerous levels detected off site
(1000’ away).
On going Water sampling/water quality monitoring in Bayou Corne and Grand
Bayou indicates no water pollution associated with the incident to date.
To date outdoor air monitoring has been conducted in response to the receipt of
97 rights of passage.
57 indoor air monitoring inspections have been conducted in response
to citizen requests.
Private residence air monitoring is available for scheduling upon citizen
completion of the Right of passage form. Please call (225) 219-3015 to notify
DEQ if you desire monitoring..
LDEQ Command Post on site. Mobile Air Monitoring Lab (MAML) scheduled to be on site on a recurring basis collecting continuous data on methane/non-methane VOCs and H2S.
DEQ is conducting community air monitoring
DEQ has submitted comments on Texas Brine’s proposed water control structure to DNR
Approved emergency water discharge permit allowing discharge of water back into the sinkhole (9/6)
Has begun water sampling weekly in the Bayou near sinkhole water discharge
Collected Hydrocarbon samples within sinkhole
Mobile Air Monitoring Lab (MAML) departed site 5/27/14
Held public hearing on TBC LPDES permit application (9/9/14)
Assumption Parish Operational Situation Summary

## Slide 18: Assumption Parish Operational Situation Summary
Department of Transportation and Development
  Regular monitoring of roadways and bridges in the area for ground movement
  Developed a traffic contingency plan if needed
  As of 25 Mar 2015 DOTD monitoring equipment has not detected any permanent bridge or highway movements nor any noteworthy trends.
  No significant changes in the surface of Hwy 70 profiler runs
  In an abundance of caution DOTD crews have established a fifth CORS site in the Bayou Corne community. This fifth CORS device was part of the original package, and is not the result of any new developments
  Held stakeholders meeting for Hwy 70 reroute options 15 May
  Performed Hwy 70 profiler run (10/21)
  Performed Hwy 70 profiler run (11/18)
  Swapped out the modem at CORS-5 station. Station is now operational (12/22)

## Slide 20: Assumption Parish Operational Situation Summary
Department of Transportation and Development (con’td)
SAA 1 | Installed April 23, 2013.
SAA 2 | Installed April 25, 2013.
SAA 3 | Installed July 2, 2013.
SAA 4 | Installed April 30, 2013.
SAA 5 | Installed April 24, 2013.
SAA GENERAL | Data from each station is being downloaded to DOTD hourly with manual analysis performed periodically. Options to provide reliable cellular communications to each site are being investigated. Automated alerts are being sent to B. Fernandez for situational awareness and action as needed. No significant movements off of baseline noted
SENSR 1 | 
SENSR 2 | 
SENSR 3 | 
SENSR GENERAL | Installed all equipment in April 2013. Training is completed. No significant movements off of baseline noted
HWY 70 REALIGNMENT | SAP Contract No. 4400001862, State Project No. H.010571.1, LA 70 Bypass, Stage 0 Feasibility Study in separate document. Stage 0 meeting was held for possible bypass road on 27 MAR. A stakeholder meeting regarding the potential Hwy 70 bypass road was held on April 11, 2013.
HWY 70 CONTINGENCY PLAN | Developed August 11, 2012 by District 61 .
EMERGENCY COMMUNICATION PLAN | Draft plan developed March 18, 2013; alert roster developed April 10, 2013.
ACTIVITY | STATUS/REMARKS
CORS 1 | Installed on Monday, April 1, 2013.
CORS 2 | Installed on Tuesday, July 17, 2013.
CORS 3 | Installed on Monday, April 8, 2013.
CORS 4 | Installed on Tuesday, April 9, 2013.
CORS 5 | Installed on Wednesday, December 10, 2014; operational 12/15/2014
ACTIVITY | Reports from the active CORS sites are published daily and provided online at the following FTP site: ftp://mimir.lsu.edu¦anonymous:user@mimir.lsu.edu:2123 Web interface account has been created. Credentials for accessing CORS911 sites via web site was distributed on April 29, 2013. No significant movements off baseline have been noted.

## Slide 21
Assumption Parish Scientific Situation Summary
As of Thursday, March 26, 2015
There were 33 MEQs yesterday and 20 MEQs? since midnight that meet the selection criteria. There was 1 VLP detected yesterday and no VLPs detected since midnight. (12/17/14)
There were 8 MEQs yesterday and 1 MEQs since midnight that meet the selection criteria. There were no VLPs detected yesterday and no VLPs detected since midnight. (12/23/14)
There were 35 MEQs yesterday and 22 MEQs since midnight that meet the selection criteria. There were no VLPs detected yesterday and 3 VLPs detected since midnight. (12/30/14)
There were 84 MEQs yesterday and 30 MEQs since midnight that meet the selection criteria. There were no VLPs detected yesterday and no VLPs detected since midnight. (1/7/15)
There were 67 MEQs yesterday and 23 MEQs since midnight that meet the selection criteria. There was 1 VLP detected yesterday and no VLPs detected since midnight. (1/14/15)
There were 7 MEQs yesterday and no MEQs since midnight that meet the selection criteria. There were no VLPs detected yesterday and no VLPs detected since midnight. (1/21/15)
There were 2 MEQs yesterday and 3 MEQs since midnight that meet the selection criteria. There were no VLPs detected yesterday and no VLPs detected since midnight. (1/28)
There were 4 MEQs yesterday and 7 MEQs since midnight that meet the selection criteria. There were no VLPs detected yesterday and no VLPs detected since midnight. (2/4/15)
There were 40 MEQs yesterday and 13 MEQs since midnight that meet the selection criteria. There were no VLPs detected yesterday and no VLPs detected since midnight. (2/11/15)
There were 97 MEQs yesterday and 37 MEQs since midnight that meet the selection criteria. There were no VLPs detected yesterday and no VLPs detected since midnight. (2/18/15)
There were 128 MEQs yesterday and 37 MEQs since midnight that meet the selection criteria. There were no VLPs detected yesterday and no VLPs detected since midnight. (2/25/15)
There were 125 MEQs yesterday and 32 MEQs since midnight that meet the selection criteria. There were no VLPs detected yesterday and no VLPs detected since midnight. (3/4/15)
There were 86 MEQs yesterday and 39 MEQs since midnight that meet the selection criteria. There were no VLPs detected yesterday and no VLPs detected since midnight. (3/11/15)
There were 108 MEQs yesterday and 36 MEQs since midnight that meet the selection criteria. There were no VLPs detected yesterday and no VLPs detected since midnight. (3/18/15)
There were 70 MEQs yesterday and 36 MEQs since midnight that meet the selection criteria. There was 1 VLP detected yesterday and no VLPs detected since midnight. (3/25/15)

## Slide 22: Assumption Parish Scientific Situation Summary
  Scientific Workgroup theories of cause:
    Salt Dome moving – natural migration of gas
    Failed cement casing in OXY #3 well
    Cavity Failure
    Salt / Caprock falling from top of the cavern
      Natural
      Man-made (including penetration into sediments by cavern)
    Gas storage cavern connections, communications by fractures
    Low permeability seepage of gas into OXY #3 (source unknown)
    Regional Tectonic activity (movement on growth faults)
    A combination of above events
    Held monthly meeting (conference call) on 2/19/14
    Quarterly meeting (conference call) on 11/19/14

## Slide 23: Next Operational Period (25 Mar – 1 Apr 15) Incident Action Plan
DNR:
  Texas Brine conducting hydrocarbon removal operations
  Perform oversight of operations at investigatory well, observation/vent well and sink hole (day light hours)
  Staff providing assist Assumption Parish Incident Commander and DEQ with bubble site monitoring, community air monitoring, and in-home monitoring
  Reviewing analysis of water samples from water wells screened in Mississippi River Alluvial aquifer
  Continue source investigation and file reviews
  Coordinate and provide information to science team
  Dome operators proceeding to implement their Shallow Geology, Aquifer, and Caprock Characterization Plan
  CB&I to collect pressure readings from the shallow water Geoprobes
  CB&I continues to evaluate the production of formation gas from the vent wells
  November 12, 2012 emergency order from the Commissioner of Conservation:
    Homes – Ventilation improvements in unventilated, unoccupied, enclosed spaces
      Gas Monitors
    Texas Brine’s contractor is Installing pressure monitoring wells with DNR oversight.
    Develop plan for mitigation problem over area
    Contain dissolved contamination from flowing into Bayou Corne
The State Agency is responsible for oversight of the following activities. Texas Brine and its contractors are performing operational response activities.

## Slide 24
Next Operational Period (25 Mar – 1 Apr 15) Incident Action Plan
DNR (Cont’d)
  Texas Brine contractor to maintain antennas & repeaters for in-home monitoring
  Texas Brine contractor to maintain in-home monitors.
  BRC continues to evaluate data and provide recommended requirements
  Monitoring under slab venting installation
  Weekly surveys
  Conduct daily well readings and flare maintenance
  Monitor continuous dewatering of ORWs
  PMWs - 04 and 07 - monitor for safety and security
  Continue Fenstermaker survey
  Begin ORW-24 Phase 4 vent test (6 month)
  Begin modified depletion tests on ORWs 37, 49, 52, 53, 56
  Collect industrial well samples
The State Agency is responsible for oversight of the following activities. Texas Brine and its contractors are performing operational response activities.

## Slide 25
DEQ:
  Continue to conduct air and water quality monitoring in the community and in the area of the bubbling in Bayou Corne, Triche Canal, and Grand Bayou
  Continue to offer indoor air monitoring to residents who complete the Rite of Passage form from the Parish. Residents desiring indoor home monitoring may call DEQ @ (225) 219-3015
  Pursuant to the DNR press release dated 11/7/2012 regarding the pressure in some geoprobes, LDEQ will conduct indoor air monitoring as requested at residential homes in the Bayou Corne community.
  Conduct any test required by scientific group to aid in source/cause identification
  Provide oversight of Texas Brine’s efforts to conduct hydrocarbon removal at the slurry site.
  Provide oversight and review of Texas Brine’s air and water quality monitoring efforts.
  Continue to visually monitor conditions of the booms and general conditions of the slurry area from the well pad.
  Perform Bayou Corne water quality background sampling
  Public hearing on September 9th at 6:00 pm
Next Operational Period (25 Mar – 1 Apr 15) Incident Action Plan

## Slide 26: Next Operational Period (25 Mar – 1 Apr 15) Incident Action Plan
DHH / Office of Public Health
  DHH will continue to review and analyze environmental sample data as provided by the Louisiana Department of Environmental Quality (LDEQ), for any chemical findings that would indicate a potential public health risk.
  DHH Safe Drinking Water Program will continue to monitor the incident for any reports of the expansion of the slurry/hole to ensure that water distribution underground piping is not compromised.

## Slide 27: Next Operational Period (25 Mar – 1 Apr 15) Incident Action Plan
DHH / Office of Public Health:
  DHH/OPH will continue to participate in meetings with GOHSEP and Assumption Parish to maintain visibility and operational readiness for any potential public health concerns.

## Slide 28: Next Operational Period (25 Mar – 1 Apr 15) Incident Action Plan
DOTD:
  Continue daily observation of road and bridges
  Will continue observation and analysis of deformation spots along Hwy 70 in evacuation zone
  Continuous monitoring of Hwy 70 with instrumentation
  Continue observation and analysis of Hwy 69
  Continue establishing a fifth CORS site in the Bayou Corne area

## Slide 29
Scientific Group:
  Analyzing groundwater sample analyses
  Evaluate issues as they arise
  Continue to provide information to the UCG
  Anyone can submit information at any time for science team evaluation by sending an email to askgohsep@la.gov
  Additional members added to the team as needed
  Will hold its next Conference Call 2/18 at 2pm
Next Operational Period (25 Mar – 1 Apr 15) Incident Action Plan

## Slide 30: Assumption Parish Long Range Plan
DNR:
  Conducting testing of investigatory well to determine cavern condition and root cause
  Scientific Group conference calls/meetings will be scheduled weekly to review new data and issues that arise
  Continue source investigation and file review
  Evaluate results of monitoring data and take necessary action
  Monitor operations at investigatory, observation/vent well and sink hole (day light hours)
  Staff on standby to assist incident commander
  Ensure total remediation of the entire site
  Continue to pursue landowner access agreements
  Implement CB&I’s Plan of Action
  Conduct industrial well sampling bi-weekly and bubble sites as reported in general vicinity of operations.
  Dome operators to identify presence of natural gas and vent as necessary
  Ensure Texas Brine fully complies with the Commissioner of Conservation’s Orders dated 11 Oct 12, Nov 2012, 7 Dec 2012, and 14 Jan 2013.
  Blue Ribbon Commission will evaluate data collected in order to provide recommendations on risk levels to the Parish
DOTD:
  Investigating bypass alignment of LA 70 around the Salt Dome
  Continuous automated monitoring of roadway-bridge movement and subsidence
DEQ:
  Continue to conduct sampling of air and water in area of operation
  Continue oversight of ongoing remedial activities
  Continue to conduct hazard assessment monitoring with APSO in resident homes and properties when requested.