## Slide 1
The Pod
Bill Ische, Business Development Manager Chris Jannace, Detection Specialist 03 September 2015
The Trafficware Pod
As a Means of Collecting Purdue High Resolution Data
The Pod
Technical Training

## Slide 2: Agenda
Components review
TSI review and planning considerations (Pod placement, spacing, antenna ranges)
Installation
  Brackets and materials required
  Antenna set-up possibilities / location constraints
  Wiring – diagrams & hands-on
  Drill equipment / Installation instructions (videos)
Software programming (best practices)
Requirements and time considerations for changes to active systems
Reports & Troubleshooting

## Slide 3: Components

## Slide 4: Components Pod Sensor
900 MHz Communication
6’ x 6’ Detection Area
10 Year Battery Life
  700 detections per hour (24/7)

## Slide 5: Components Access Point
120VAC
Wireless (internal) or Wired Communication
3 Radios (external)
Box designed to fit articulating style bracket (comes with Access Point kit)

## Slide 6: Components Base Station
ZigBee standard compliant encryption used between Base Station and Access Point
Can communicate effectively with two Access Points
Browser-based GUI (You own the Base Station, You own the GUI)
SDLC or parallel wiring connection to controller / cabinet based on configuration

## Slide 7
Detection Zones Pod Spacing

## Slide 8
TSI Review & Planning Considerations
*** Go to Google Earth to review ranges

## Slide 9
TSI Review & Planning Considerations

## Slide 10
TSI Review & Planning Considerations

## Slide 11
TSI Review & Planning Considerations Ex. 2
Up to 30 high-volume Pods per Radio
Add Omni or Panel Antenna

## Slide 12: Pod Installation
Diamond core needs water, Slower
Percussion Core Drill faster, No water necessary
Core Drill 4.5 inch diameter Hole 2.75 inches deep

## Slide 13: Software Programming Set-up Tips

## Slide 14: Software Programming Computer Set-up

## Slide 15: Software Programming Base Station
Serial Number (Sticker)
Cable to Laptop
Antenna to top of Cabinet
Cable to Controller
Cable to Switch / Cell Modem
Cable to Expansion Cards (if not SDLC)
Cable to Access Point (thru EIA-485 Lightning Suppression Panel

## Slide 16: Set-up Tips Net ID / Access Point
Explanation of NetID effects on Access Point Radios
NetID: 1
NetID: 2
NetID: 3
NetID: 4
NetID: 5

## Slide 17: Software Programming Access Point
Serial
Number
Comm ID
RF Cable to Antennas
Radio 1
(Omni)
Radio 3
(Panel)
Radio 2
(Panel)
16 awg Cable (Power) to Power Panel (Cabinet)
EIA-485 Cable to Lightning Suppression Panel (Cabinet)

## Slide 18: Software Programming Pod
For scanner
Mark Pods –
Phase / Direction / Order
(Recommended)

## Slide 19: Changes – Requirements & Time Considerations
Reload Config
  System Reboot – loss of detection for minute
  15 minute process (+Pod sync) – constant calls
NetID Considerations
When Required
  Base Station NetID change
  Access Point replacement
  Access Point Communication change
  Pod replacement
  Pod Add / Delete
  Pod Radio change

## Slide 20: Troubleshooting
Stuck Pod (Blue) / Unresponsive Pod (Gray)
  RSSI / Antennas
  Sensitivity – decrease / increase
  Reset Sensor (“Learn” button)
  Reports – check Vol/Occ for inconsistent performance
No Comm Pod (Yellow)
  Serial Number
  Reports – check Vol/Occ for inconsistent performance; check Events report for “IncorrectID”
No Comm Access Point (Yellow)
  Check Serial Number
  Wireless – power, state of antenna
  Wired – power, loop back, lightning suppression panel

## Slide 21: Troubleshooting in Reports
Volume / Occupance Report
*** Find corresponding Events Report information

## Slide 22: Troubleshooting in Reports
Events Report
Fix:
Change NetID
Reload Config

## Slide 23: Contact Information
Chris Jannace, Detection Specialist
ChrisJannace@trafficware.com
(O) 281-240-7233 x309
(C) 626-261-0875
Areas of Responsibility:
Louisiana
Mississippi
Texas
Arkansas
Oklahoma
New Mexico
Hawaii